## Slide 1: Bearing Fault Diagnosis with Vibration Data
Part I · Smart-factory fault diagnosis
NASA/IMS run-to-failure bearing dataset
Notes: Our Part I topic: diagnosing rolling-element bearing faults from vibration, using a real run-to-failure dataset.

## Slide 2: Problem: bearings fail without warning and stop the line
Bearings sit in every motor, pump, fan and spindle. Goal: using only vibration sensors and no fault examples, answer three questions.
When?
When did the bearing stop being healthy?
Where?
Which bearing on the shaft is failing?
What?
Outer race, inner race or rolling element?
Notes: Bearing failures stop production. We want vibration-only diagnosis that answers when, where and what, without needing recorded fault examples, because real failures are rare.

## Slide 3: Dataset: 4 bearings on one shaft, run until failure
3
run-to-failure tests
9,464
1-second snapshots at 20 kHz
4
bearings failed
8
bearings stayed healthy
Test | Duration | Failed bearing | Real fault
Set 1 | 828 h | B3 | Inner race
Set 1 | 828 h | B4 | Rolling element
Set 2 | 164 h | B1 | Outer race
Set 3 | 1,073 h | B3 | Outer race
NASA/IMS (Center for Intelligent Maintenance Systems) data · Rexnord ZA-2115 bearings · 2,000 rpm (revolutions per minute) · B1-B4 = bearing 1-4
Notes: Three tests, about 9,500 snapshots recorded every 10 minutes until a bearing failed. Four failures are what we must find; the eight surviving bearings must not be flagged.

## Slide 4: What we do with the data: turn vibration into a fault rhythm
1. Raw vibration
1 s snapshot from each sensor
2. Envelope
trace the outline of the impact 'clicks'
3. Spectrum
which rhythms (Hz = per second) are present
4. Match
compare peaks with each part's rhythm
Damaged part | Rhythm name | Clicks per second
Outer race | BPFO (Ball Pass Frequency, Outer) | 236 Hz
Inner race | BPFI (Ball Pass Frequency, Inner) | 297 Hz
Rolling element | 2BSF (2 × Ball Spin Frequency) | 280 Hz
Cage | FTF (Fundamental Train Frequency) | 15 Hz
Key idea
Like a pebble in a bike tyre: count the ticks per second and you know which part is damaged.
Notes: Each bearing part moves at a different speed, so a crack on it produces impacts at its own rate. The envelope spectrum shows those rates as peaks.

## Slide 5: A damaged bearing shows sharp peaks at its fault rhythm
Chart: Rhythm frequency (Hz)
Set 2, bearing 1
Peaks at 230, 461, 692 Hz
= outer-race rhythm and its multiples.
But not at 236 Hz: the real shaft runs about 2.5% slower than the nameplate.
Notes: Healthy bearing: flat noise. Failing bearing: clear peaks at 230 Hz and its multiples, the outer-race rhythm. The real speed is 2.5% below nominal, so our method must search for the true speed.

## Slide 6: Loudness tells where and when; rhythm tells what
Stage A · WHERE and WHEN
Stage B · WHAT
Loudness growth
RMS (vibration energy) vs its own healthy start
Compare with neighbours
subtract the other bearings' growth
Alarm
≥ 16% louder than neighbours for 1 hour
Envelope spectrum
best frequency band, peaks vs local noise
Match fault rhythms
search the real speed (95-101% of nameplate)
Fault evidence
compared with all healthy bearings
Diagnosis
which bearing · since when · which fault
Notes: Two stages. Stage A uses loudness, which differs between bearings, to find which bearing and when. Stage B uses the rhythm, which every sensor hears, to identify the fault. No fault labels are needed: only physics and statistics of the healthy period.

## Slide 7: Result 1: the failing bearing pulls away from its neighbours
Chart: Hours before end of test (set 2)
4 / 4
failures detected
61 h
median warning before the end
2 / 8
healthy bearings falsely alarmed
Notes: Set 2 example: bearing 1 crosses the alarm limit about 70 hours before the end, while its neighbours stay flat or drop. Over all three tests: 4 of 4 failures detected, median 61 hours early, 2 false alarms on 8 healthy bearings.

## Slide 8: Result 2: all 4 fault types named correctly
Failed bearing | Real fault | Our diagnosis | Warning before end
Set 1 · B4 | Rolling element | Rolling element ✔ | 97 h
Set 2 · B1 | Outer race | Outer race ✔ | 70 h
Set 3 · B3 | Outer race | Outer race ✔ | 53 h
Set 1 · B3 | Inner race | Inner race ✔ | 12 h
Healthy bearings: 6 of 8 never alarmed. One alarm came during a neighbour's final breakdown; the other was a short bump the system refused to name.
Notes: Every failed bearing is found and its fault type named. The inner-race fault shows up late, only 12 hours before the end.

## Slide 9: Result 3: our answer is clear; the usual method guesses
Chart: Separation (log scale)
| Set 2 B1 | Set 3 B3 | Set 1 B3 | Set 1 B4
Usual method (fixed band, textbook rhythms) | 1.88 | 1.03 | 2.5 | 1.03
Proposed system | 50.19 | 9.86 | 3.86 | 2.68
Separation
= true fault's evidence ÷ strongest wrong fault's evidence
1.0 = coin flip
Usual method: 1.03× twice. Ours: at least 2.7×.
Notes: Both methods name the right fault, but the usual method wins twice by only 3%, a coin flip. Ours separates the true fault at least 2.7 times above the alternatives, thanks to the speed search and measuring peaks against local noise.

## Slide 10: Loudness finds it; rhythm names it
All 4 failures found, median 61 h early, every fault named
Works without fault examples: physics + healthy data only
Limit: only 4 failures, so treat results as a case study
Part II: predict RUL (Remaining Useful Life) from the alarm
Notes: Summary and link to Part II: the Stage A loudness index is the signal a remaining-useful-life model can extrapolate.