## Slide 1: Choosing a Maintenance Strategy for Bearings
Part II · Predictive maintenance with AI
NASA/IMS run-to-failure bearing dataset
Notes: Part II builds on our Part I bearing diagnosis. Part I gave us alarms that say a bearing is failing. Part II asks the maintenance manager's question: should we repair after breakdown, replace on a schedule, or act on the alarms, and how much does physics or AI monitoring actually save?

## Slide 2: The question: when should a factory replace a bearing?
We replay each strategy on the same 12 bearings (4 failed, 8 healthy) and count breakdowns, needless replacements and cost.
1
Reactive
Run until it breaks, then repair
Breakdowns stop the line
2
Preventive
Replace every T hours on a schedule
Lives vary 164-1,073 h: waste or breakdowns
3
Predictive
Replace when monitoring raises an alarm
Needs an early, reliable alarm: Part I
Notes: There are three classic strategies. Reactive: run until it breaks. Cheap per repair, but a breakdown stops the line and can damage the shaft. Preventive: replace on a fixed schedule, but bearing lives vary a lot, here from 164 to over 1,000 hours, so you either replace too often or still get breakdowns. Predictive, or condition-based: replace when monitoring raises an alarm. It only works if the alarm is early and reliable. We test all three on the same 12 bearings.

## Slide 3: Each alarm is late or silent on a different bearing
Chart: Hours of warning before failure
| Set 1 B3 inner | Set 1 B4 roller | Set 2 B1 outer | Set 3 B3 outer
Physics alarm (peer contrast) | 12 | 97 | 70 | 53
AI alarm (autoencoder) | 71 | 119 | 54
AI: missed
2 vs 0
healthy bearings falsely alarmed (physics vs AI)
Complementary
AI warns 59 h earlier on the inner-race fault
Physics catches set 3 B3, which AI misses
Rule: act on either alarm
Notes: Part I gave us two condition monitors. The physics alarm compares each bearing's vibration energy with its neighbours. The AI alarm is an autoencoder trained only on healthy data: it flags a bearing whose vibration it cannot reconstruct. Neither uses fault labels. The bars show how many hours before failure each one warns. The AI warns about the inner-race fault 71 hours ahead, where physics gives only 12. Physics catches set 3 bearing 3, which the AI misses completely. And the AI never alarmed on a healthy bearing; physics did twice. We checked that the early AI alarm on set 1 bearing 3 comes mainly from its own impact signal, kurtosis and peaks, not from its failing neighbour bearing 4 heard through the housing. So the two are complementary: use either one's alarm.

## Slide 4: How we score a strategy
Caught in time
Alarm ≥ 24 h before failure: planned replacement
cost 1
Breakdown
No alarm, or alarm too late for the crew
cost 10
Needless replacement
Alarm on a healthy bearing
cost 1
Cost per 1,000 h = 1,000 × total cost ÷ total operating hours
Lead time 24 h and breakdown factor 10 are assumptions: both are varied on the next slides
Same 12 bearings for every strategy. Preventive gets its best interval chosen with hindsight, so it is shown at its most optimistic.
Notes: The scoring rules. When an alarm fires, the crew needs 24 hours to get parts and schedule the work, then replaces the bearing. If the bearing breaks before that, it counts as a breakdown. An alarm on a healthy bearing is a needless replacement. A planned replacement costs 1 unit; a breakdown costs 10, for downtime, damage and rush parts. We divide total cost by total operating hours, the standard renewal-reward cost rate. Later we vary both the 24 hours and the factor of 10, because they differ between factories.

## Slide 5: Result: acting on either alarm catches all 4 failures
Strategy | Caught | Breakdowns | Needless | Cost / 1,000 h
Reactive (run to failure) | 0 / 4 | 4 | 0 | 4.84
Preventive (every 824 h)* | 3 / 4 | 1 | 5 | 2.48
Physics alarm | 3 / 4 | 1 | 2 | 2.03
AI alarm | 3 / 4 | 1 | 0 | 1.61
Physics OR AI alarm | 4 / 4 | 0 | 2 | 0.82
Oracle (knows the future) | 4 / 4 | 0 | 0 | 0.48
*Best fixed interval chosen with hindsight (just before set 1 ends). Planned replacement = 1, breakdown = 10, lead time 24 h.
4 / 4
failures caught, 0 breakdowns
6×
cheaper than reactive (0.82 vs 4.84)
2 / 8
needless replacements, both from the physics alarm
Notes: The result at 24 hours lead time and breakdown cost 10. Reactive: four breakdowns, 4.8 per thousand hours. Preventive, even with the best interval chosen in hindsight: one breakdown and five needless replacements. Physics alone or AI alone: three of four caught. Acting on either alarm catches all four with no breakdowns, at 0.82, about a sixth of reactive; the oracle that knows exactly when each bearing fails would cost 0.48.

## Slide 6: Acting on either alarm pays above 2× breakdown cost
Chart: Breakdown cost ÷ planned replacement cost (log scale)
| 1.5 | 2.0 | 3.0 | 5.0 | 7.0 | 10.0 | 15.0 | 20.0 | 30.0 | 50.0 | 70.0 | 100.0
Reactive | 0.727 | 0.969 | 1.453 | 2.422 | 3.391 | 4.844 | 7.267 | 9.689 | 14.533 | 24.222 | 33.911 | 48.445
Preventive (hindsight) | 0.727 | 0.969 | 1.453 | 1.794 | 2.07 | 2.484 | 3.174 | 3.864 | 5.244 | 6.25 | 6.25 | 6.25
Physics alarm | 0.878 | 0.945 | 1.08 | 1.35 | 1.62 | 2.025 | 2.701 | 3.376 | 4.726 | 7.427 | 10.127 | 14.178
AI alarm | 0.557 | 0.618 | 0.742 | 0.989 | 1.237 | 1.608 | 2.226 | 2.845 | 4.082 | 6.555 | 9.029 | 12.739
Physics OR AI | 0.818 | 0.818 | 0.818 | 0.818 | 0.818 | 0.818 | 0.818 | 0.818 | 0.818 | 0.818 | 0.818 | 0.818
Oracle | 0.484 | 0.484 | 0.484 | 0.484 | 0.484 | 0.484 | 0.484 | 0.484 | 0.484 | 0.484 | 0.484 | 0.484
> 2×
breakdown cost where acting on either alarm beats reactive
Reading the chart
Flat coral line: no breakdowns, so cost doesn't grow
Up to ~3×: the AI alarm alone is cheapest (no false alarms)
Grey flattens only through hindsight tuning
Notes: How the answer depends on how expensive a breakdown is, on log scales. When a breakdown costs barely more than a planned repair, nothing beats just running to failure, except the AI alarm with its zero false alarms. From about twice the cost, acting on either alarm is cheaper than reactive and preventive, and its cost stays flat because it has no breakdowns. A breakdown that stops a line often costs far more than a planned repair, but the factor depends on the factory. The grey preventive line flattens at the right only because its interval was tuned with hindsight to just before the shortest test ended.

## Slide 7: The crew must replace the bearing within about 2 days
Chart: Lead time: hours from alarm to replacement
| 4 h | 8 h | 12 h | 24 h | 48 h | 72 h
Physics alarm | 4 | 4 | 3 | 3 | 3 | 1
AI alarm | 3 | 3 | 3 | 3 | 3 | 1
Physics OR AI | 4 | 4 | 4 | 4 | 4 | 1
≤ 48 h
lead time where acting on either alarm catches all 4
At default thresholds
≤ 8 h: physics alone is enough
12-48 h: only physics OR AI catches all 4
72 h: each rule catches only 1 of 4
Notes: How fast does the crew have to act after the alarm? With up to 8 hours, the physics alarm alone catches all four. Between 12 and 48 hours, physics and AI each catch three, and only their combination catches all four: this is where the AI adds value. At 72 hours everything collapses to one of four, because the alarms come 53 to 119 hours before failure. So acting on either alarm catches all four only if replacement happens within about two days of the alarm. Note this is at our default thresholds; the next slide shows what changes when we move them.

## Slide 8: Robustness: either alarm catches all 4 in every setting tried
Check | Result
27 threshold settings (lead 24 h, breakdown 10×) | Physics OR AI: 4/4 in 27/27, cost 0.81-1.08. Physics alone: 4/4 in 9/27. AI floor changed nothing: 9 distinct outcomes
Drop one test, re-score the other two (sensitivity check) | Physics OR AI beats reactive (3.9-7.6) and preventive (1.2-3.5) every time; single alarms do not (set 2 dropped: preventive 1.21 vs physics 1.91, AI 1.61)
False alarm 5× a planned job | AI alone cheapest (1.61 vs 1.91 for either alarm)
Set 1 B3 cross-talk from B4? | Mostly no: B3's AI alarm is led by its own impacts (kurtosis, peak), not B4's roller rhythm
27 / 27
threshold settings where either alarm catches all 4
AI as insurance
Physics alone needs a lucky threshold to catch all 4
Either alarm catches all 4 in every setting tried
Notes: We tested the result against the obvious objections. First, the thresholds were tuned on these same bearings, so we moved all three of them: 27 combinations, 9 distinct outcomes because the AI floor changed nothing. Acting on either alarm catches all four failures in every one, at 0.81 to 1.08 per thousand hours. Physics alone catches all four in only 9 of 27. So the AI alarm is insurance: a factory cannot tune its threshold on failures it has not seen. Second, dropping one test at a time and re-scoring the other two, acting on either alarm always beats reactive and preventive, but the single alarms do not: without set 2 the hindsight-tuned preventive interval beats each of them, and without set 3 the AI alone is cheapest. Third, if a false alarm costs about four times a planned job or more, the AI alone, with no false alarms, is cheapest. So we claim robustness, not a single winner.

## Slide 9: What didn’t work: predicting the hours left
Calibrated RUL bound
17-59 h
safety margin, as wide as the lead time
Never catches more than “act at the alarm”; at 4-8 h lead it catches fewer (3 vs 4)
After the alarm the bearings lasted 12, 53, 70, 97 h: too spread to learn from 3 examples
Foundation model (Chronos-2)
56 vs 25 h
RUL error vs gradient boosting (set 2 B1, exploratory run)
Forecast the vibration levelling off; it actually accelerated
Pretrained forecasters continue patterns; failure breaks the pattern
Notes: We also tried the textbook predictive-maintenance approach: predict the remaining useful life in hours, then act when it is short. Two attempts, both negative, and we think both are findings. First, gradient boosting with a calibrated safety margin. Its margin came out at 17 to 59 hours, as wide as the lead time, so it fires almost right at the alarm: it never catches more failures than simply acting on the alarm, catches fewer with a short lead time, and otherwise saves at most about five hours of bearing life. The reason is in the data: after the alarm, the four bearings lasted 12, 53, 70 and 97 hours, too spread for three training examples. Second, in an exploratory run outside the pipeline, Chronos-2, a large pretrained time-series model: it forecast the vibration levelling off instead of accelerating, and its error was more than twice that of gradient boosting, both scored at forecast points every two hours over the last 100 hours.

## Slide 10: What Part II adds, and its limits
1
Cost model
Reactive, preventive and condition-based replayed on real run-to-failure data
2
Complementary alarms
Either alarm catches all 4 in all 27 threshold settings tried: AI is insurance
3
Operating envelope
Either-alarm rule pays above 2×; catches all 4 if replaced within ~2 days
4
Two negative results
RUL prediction and a foundation model don’t help with 4 failures
Limits
Only 4 failures: a case study, not a validated accuracy
Thresholds set on these 12 bearings (4/4 still holds in 27/27 settings)
Cheapest single alarm rule varies by test and false-alarm cost
Costs and lead time are assumptions, so we show ranges
Each bearing costed alone; one stop could replace several
Preventive interval chosen with hindsight (optimistic)
Notes: To be clear about our contribution: Part II builds no new detector; the two alarms come from Part I. What it adds is the decision analysis: a cost model that replays reactive, preventive and condition-based maintenance on real run-to-failure data; the finding that the physics and AI alarms complement each other; the operating envelope, breakdown cost above twice a repair and replacement within two days; and two documented negative results. The limits: only four failures, both detectors' thresholds were set on these same bearings, and the cost numbers are assumptions, which is why we show them as ranges.

## Slide 11: Watch with two eyes; act within two days
Physics OR AI alarm: 4 of 4 failures caught, 0 breakdowns
About 6× cheaper than run-to-failure
Pays when a breakdown costs over 2× a planned repair
Holds over 27 threshold settings; limit: only 4 failures
Notes: Summary. Part I's two alarms, physics and AI, see different failures. Acting on either one catches all four failures with no breakdowns, about six times cheaper than running to failure, as long as a breakdown costs more than twice a planned repair and the crew can replace the bearing within two days. Predicting exact hours left did not work with four failures, and we showed why. Thank you.